## STATUS REGISTER
I	T	H	S	V	N	Z	C

- Bit 15 -
- Bit 14 -
- Bit 13 -
- Bit 12 -
- Bit 11 -
- Bit 10 -
- Bit 9 -
- Bit 8 -
- Bit 7 – I: Global Interrupt Enable
- Bit 6 – T: Bit Copy Storage
- Bit 5 – H: Half Carry Flag
- Bit 4 – S: Sign Bit
- Bit 3 – V: Two's Complement Overflow Flag
- Bit 2 – N: Negative Flag
- Bit 1 – Z: Zero Flag
- Bit 0 – C: Carry Flag

## ADD

Description
Add two 8 Bit Integers(Ra and Rb) and place the result in Rd

Operation	Syntax
Rd ← Ra + Rb	ADD Rd,Ra,Rb

Operands
0 ≤ Rd ≤ 255
0 ≤ Ra ≤ 255
0 ≤ Rb ≤ 255

32 Bit Opcode

0000	0000	dddd	dddd	aaaa	aaaa	bbbb	bbbb

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1
## SUB
Description
Subtract two 8 Bit Integers(Ra - Rb) and place the result in Rd

Operation	Syntax
Rd ← Ra + Rb	ADD Rd,Ra,Rb

Operands
0 ≤ Rd ≤ 255
0 ≤ Ra ≤ 255
0 ≤ Rb ≤ 255

32 Bit Opcode

0000	0000	dddd	dddd	aaaa	aaaa	bbbb	bbbb

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1
## AND
Description
Bitwise AND two 8 bit registers and place the result in a third 8 bit register

Operation	Syntax
Rd ← Ra • Rb	AND Rd,Ra,Rb

Operands
0 ≤ Rd ≤ 255
0 ≤ Ra ≤ 255
0 ≤ Rb ≤ 255

32 Bit Opcode

0000	0000	dddd	dddd	aaaa	aaaa	bbbb	bbbb

SREG
S: N ⊕ V, For signed tests.
V: 0
N: R7 - Set if MSB of the result is set; cleared otherwise.
Z: NAND(Rd) - Set if the result is $00; cleared otherwise

Words
1 (4 Bytes)

Cycles
1

## LDI
###### Description
Load Immediate, load a constant K data into Rd

Operation	Syntax
Rd ← K	LDI Rd,K

Operands
0 ≤ Rd ≤ 255
0 ≤ K ≤ 65535

32 Bit Opcode

0000	0000	dddd	dddd	KKKK	KKKK	KKKK	KKKK

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## OUT
###### Description
Stores data from Rr into the I/O Space A

Operation	Syntax
I/O(A) ← Rr	OUT A,Rr

Operands
0 ≤ Rr ≤ 255
0 ≤ A ≤ 65535

32 Bit Opcode

0000	0000	AAAA	AAAA	AAAA	AAAA	rrrr	rrrr

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## IN
###### Description
Stores data from I/O Space into Rd

Operation	Syntax
Rd ← I/O(A)	IN Rd,A

Operands
0 ≤ A ≤ 65535
0 ≤ Rd ≤ 255

32 Bit Opcode

0000	0000	AAAA	AAAA	AAAA	AAAA	rrrr	rrrr

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## INC
###### Description
Increment Register by 1

Operation	Syntax
Rd ← Rd + 1	INC Rd

Operands
0 ≤ Rd ≤ 255

32 Bit Opcode

0000	0000	dddd	dddd	0000	0000	0000	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## DEC
###### Description
Decrement Register by 1

Operation	Syntax
Rd ← Rd - 1	DEC Rd

Operands
0 ≤ Rd ≤ 255

32 Bit Opcode

0000	0000	dddd	dddd	0000	0000	0000	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## LD
###### Description
Loads one byte indirect from an addressed data-space location to a register

Operation	Syntax
Rd ← I	LD Rd,I

Operands
0 ≤ Rd ≤ 255
0 ≤ _ ≤ 255

32 Bit Opcode

0000	0000	dddd	dddd	IIII	IIII	0000	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## ST
###### Description
Store one byte indirect from a register to an addressed data-space location. I is a Register containing an address to a data-space location. Rr

Operation	Syntax
I ← Rr	ST I,Rr

Operands
0 ≤ Rr ≤ 255
0 ≤ I ≤ 255

32 Bit Opcode

0000	0000	IIII	IIII	rrrr	rrrr	0000	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## STS
###### Description
Store one byte directly from a register to an addressed data-space location, specified by the programmer.

Operation	Syntax
k ← Rr	STI k,Rr

Operands
0 ≤ Rr ≤ 255
0 ≤ k ≤ 65535

32 Bit Opcode

0000	0000	kkkk	kkkk	kkkk	kkkk	rrrr	rrrr

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## MOV
###### Description
Copies Rr into Rd

Operation	Syntax
Rd ← Rr	MOV Rd,Rr

Operands
0 ≤ Rr ≤ 255
0 ≤ Rd ≤ 255

32 Bit Opcode

0000	0000	dddd	dddd	rrrr	rrrr	0000	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## CBI
###### Description
Clears a specified bit in an I/O Register

Operation	Syntax
Rd ← Rr	CBI I/O(A),b

Operands
0 ≤ A ≤ 65535
0 ≤ b ≤ 15

32 Bit Opcode

0000	0000	AAAA	AAAA	AAAA	AAAA	bbbb	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## SBI
###### Description
Sets a specified bit in an I/O Register

Operation	Syntax
Rd ← Rr	SBI I/O(A),b

Operands
0 ≤ A ≤ 65535
0 ≤ b ≤ 15

32 Bit Opcode

0000	0000	AAAA	AAAA	AAAA	AAAA	bbbb	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1

## NOP
###### Description
This description is intentionally left blank.

Operation	Syntax
NOP

Operands

32 Bit Opcode

0000	0000	0000	0000	0000	0000	0000	0000

SREG
SAME AS AVR

Words
1 (4 Bytes)

Cycles
1.0